## Slide 1
Iterative algorithm for the generalized segmental continuous cutting problem with optimization time constraint
Intelligent and Fuzzy Systems (INFUS 2024)
July 16 – 18, 2024
Istanbul , Turkey
Alexander Petunin, Stanislav Ukolov

## Slide 2
Control program development
for sheet cutting machines
Maximal material utilization
Minimal path cost in terms of money and resources, including cutting time
Nesting
Tool path routing
NC Program generation

## Slide 3
Classification of
tool path routing problems
Continuum of piercing points
GSCCP
GSCCP
TSP
GTSP
CCP
ECP
SCCP
ICP
GSCCP
Finite set of piercing points
Fixed piercing points

## Slide 4
Definition of tool path (route) by cutting segments
Parts:
…
Closed contours:
…
Tool path components:
  - pierce points,
  - segment entry points
  - tool off points
Definition 1: Cutting segment is trajectory between pierce point and tool off point
Note: Segment has a direction at every point.
Definition 2: ,
where - sequence of segments cutting.
Example of route containing 24 cutting segments
n = 24, N = 30, K = 24
Brown parts are cut by one cutting segment

## Slide 5
Definition the Cutting path (Route) by using concept the basic cutting segment
Definition 3: Basic segment is part of cutting segment without lead-in and lead-out
Note: Basic segment has no direction.
When basis segment contains one or more closed contours, direction of cutting (“+” for clockwise, “-” for counter clockwise) must be specified for each of them.
Every basic segments contains list of its closed contours (may be empty). is length of this list.
where (cutting direction).

## Slide 6
Non-standard cutting techniques
Multi-contour cutting - several contours are combined into one
Multi-segment cutting - one of the contours is divided into several parts
Multi-contour cutting of two parts using a “bridge”
In this study, bridges of zero width were used, so when adding one “bridge” to the nesting layout
The number of circuits is reduced by 1
The number of insertion points Npt is reduced by 1 either
The tool stroke length Lon is increased by double bridge length (which is usually chosen as the minimum)
In the practical use of bridges, the stroke length Lon may even decrease, depending on the geometry of the bridge.

## Slide 7
Example of non-trivial cutting segment
Cutting of six pentagons using single cutting segment and combined cut technique

## Slide 8
SCCP, GSCCP
Definition 4: SCCP(Segment Continuous Cutting Problem) is a problem with fixed number K and fixed set of Basic segments
Lead-in 1
Lead-out 1
Lead-out 2
Lead-in 2
In Fig. two basic segments are allocated with dashed lines of orange and yellow color.
…are Basic segments and N=K then SCCP is equivalent to CCP
Definition 5: GSCCP (Generalized SCCP) is { SCCPi i=1,2,…,T }
Thus, by introducing the class of GSCCP, we have significantly expanded the existing classification of tool path problem for CNC sheet cutting machines. Actually SCCP and GSCCP are subclasses ICP containing all tasks with finite sets of basic cutting segments, i.e. CCP SCCP GSCCP ICP
Basic segment 1
Basic segment 2

## Slide 9
Example of GSCCP task
Standard Cutting Technique:
45 base segments
Introducing Multi-Contour Cutting:
39 base segments
Reduce to GTSP:
425 possible pierce points
The problem of forming "promising" subtasks of GSCCP for searching a global extremum belongs to the class of clustering problem. In the future, neural networks are supposed to be used to generate the ensemble of subtasks GSCCP

## Slide 10
Two optimization criteria
Cost of cutting process Fcost = where:
Loff — length of tool path with the switched off cutting tool (idle tool path, blue color);
Coff — cost of unit length of tool path with the switched off cutting tool;
Lon — length of tool path with the switched on cutting tool (including length lead-in and lead-out, red color);
Con — cost of unit of a path with the switched on cutting tool;
Npt — number of pierces;
Cpt — cost of one pierce.
Time of cutting process tcut=
where:
Von — speed of cutting process with the switched on cutting tool;
Voff — speed of tool’s movement with the switched off cutting tool;
ton — time for one piercing of sheet material.

## Slide 11
Algorithm pseudocode
# Generating task instances
for i = 1 to N
# Correction of the objective function
# to the complete problem
end for
# Main loop
for j = 1 to K
# Update the upper bounds
for i = 1 to N
end for
# Partial calculation of task instances
for i = 1 to N
if then
# The task has been
# completed
continue
end if
# Cutting off “uninteresting” subtasks
if then
delete
end if
end for
end for
return
Input | 
 | parts placed on the sheet
 | iteration count
 | number of instances of segment cutting tasks
 | time slice for one task
Total calculation time | 
Input | 
 | parts placed on the sheet
 | iteration count
 | number of instances of segment cutting tasks
 | time slice for one task
# Finding upper bounds
for i = 1 to N
end for
Output | 
 | toolpath
Output | 
 | toolpath

## Slide 12
Cutoff condition
Correction for every task instance

## Slide 13
Numerical experiment
Nesting layout | Parts | Contours | Lon, mm | Piercing points
p3xl_1 | 16 | 32 | 12040 | 586
p3xl_2 | 17 | 35 | 8783 | 861
p3xl_3 | 16 | 32 | 10698 | 521
p3xl_4 | 18 | 36 | 7193 | 696
p3xl_5 | 19 | 38 | 17233 | 557
p3xl_5
PCGLNS solution

## Slide 14
Technological parameters
Material | Thickness, mm | Tpt, s | Von, m/s |  | Voff, m/s
 |  |  | Good quality | Medium quality | 
Carbon steel Ст10кп | 1 | 0,8 | 0,112 | 0,158 | 0,85
 | 1,2 | 0,9 | 0,088 | 0,127 | 
 | 1,5 | 1,1 | 0,088 | 0,127 | 
 | 2 | 1,2 | 0,072 | 0,103 | 
 | 2,5 | 1,7 | 0,060 | 0,087 | 
 | 3 | 2,1 | 0,048 | 0,070 | 
 | 3,5 | 2,2 | 0,044 | 0,063 | 
 | 3,9 | 2,2 | 0,044 | 0,063 | 
 | 4 | 2,5 | 0,040 | 0,057 | 
 | 5 | 2,7 | 0,037 | 0,053 | 
 | 8 | 3 | 0,025 | 0,037 | 
 | 10 | 3,2 | 0,022 | 0,030 | 
 | 15 | 4 | 0,013 | 0,018 | 
Aluminium Амг3М | 1 | 1,3 | 0,105 | 0,175 | 
 | 2 | 2 | 0,065 | 0,108 | 
 | 3 | 3 | 0,032 | 0,052 | 
 | 5 | 4 | 0,017 | 0,028 | 
Stainless Steel 12Х18Н10Т | 1 | 1 | 0,105 | 0,175 | 
 | 1,5 | 1,5 | 0,083 | 0,140 | 
 | 2 | 1,8 | 0,062 | 0,103 | 
 | 2,5 | 2,2 | 0,050 | 0,083 | 
 | 3 | 2,8 | 0,042 | 0,068 | 
 | 4 | 3,3 | 0,028 | 0,047 | 
 | 5 | 4 | 0,022 | 0,035 | 
 | 6 | 4,5 | 0,017 | 0,027 | 
 | 8 | 5 | 0,008 | 0,015 | 
 | 10 | 6 | 0,005 | 0,010 | 
CNC laser cutting machine Bystronic ByStar3015

## Slide 15
Technological parameters
CNC laser cutting machine Bystronic ByStar3015

## Slide 16
Generating subtasks
Name | Bridges | UB, mm | LB0, mm | Npt | Lon, мм
p3xl_1 | 0 | 2289 | 1296 | 32 | 12040
p3xl_1-A | 3 | 2284 | 1314 | 29 | 12104
p3xl_1-B | 4 | 2287 | 1304 | 28 | 12131
p3xl_1-C | 6 | 2283 | 1360 | 26 | 12172
p3xl_2 | 0 | 1629 | 919 | 35 | 8783
p3xl_2-A | 3 | 1629 | 932 | 32 | 8845
p3xl_2-B | 4 | 1627 | 892 | 31 | 8873
p3xl_2-C | 8 | 1628 | 968 | 27 | 8971
p3xl_3 | 0 | 2114 | 1152 | 32 | 10698
p3xl_3-A | 4 | 2014 | 1192 | 28 | 10782
p3xl_3-B | 4 | 2017 | 1156 | 28 | 10799
p3xl_3-C | 6 | 2010 | 1149 | 26 | 10837
p3xl_4 | 0 | 1702 | 937 | 36 | 7193
p3xl_4-A | 3 | 1701 | 938 | 33 | 7263
p3xl_4-B | 5 | 1699 | 972 | 31 | 7297
p3xl_4-C | 8 | 1698 | 989 | 28 | 7405
p3xl_5 | 0 | 3272 | 1908 | 38 | 17233
p3xl_5-A | 3 | 3260 | 1919 | 35 | 17302
p3xl_5-B | 6 | 3261 | 1915 | 32 | 17371
p3xl_5-C | 7 | 3253 | 1935 | 31 | 17439

## Slide 17
Solutions
Subtasks of p3xl_2

## Slide 18
Mutual influence of subtasks
Name | UB | LB0 | Lon | Δ | UB'
p3xl_1 | 2289 | 1296 | 12040 | 97467 | 2289
p3xl_1-A | 2284 | 1314 | 12104 | 97985 | 1771
p3xl_1-B | 2287 | 1304 | 12131 | 98203 | 1552
p3xl_1-C | 2283 | 1360 | 12172 | 98535 | 1220
p3xl_2 | 1629 | 919 | 8783 | 71100 | 1629
p3xl_2-A | 1629 | 932 | 8845 | 71602 | 1127
p3xl_2-B | 1627 | 892 | 8873 | 71829 | 900
p3xl_2-C | 1628 | 968 | 8971 | 72622 | 107
p3xl_3 | 2114 | 1152 | 10698 | 86603 | 2114
p3xl_3-A | 2014 | 1192 | 10782 | 87283 | 1434
p3xl_3-B | 2017 | 1156 | 10799 | 87420 | 1296
p3xl_3-C | 2010 | 1149 | 10837 | 87728 | 989
p3xl_4 | 1702 | 937 | 7193 | 58229 | 1702
p3xl_4-A | 1701 | 938 | 7263 | 58796 | 1135
p3xl_4-B | 1699 | 972 | 7297 | 59071 | 860
p3xl_4-C | 1698 | 989 | 7405 | 59945 | 14
p3xl_5 | 3272 | 1908 | 17233 | 139505 | 3272
p3xl_5-A | 3260 | 1919 | 17302 | 140064 | 2713
p3xl_5-B | 3261 | 1915 | 17371 | 140622 | 2155
p3xl_5-C | 3253 | 1935 | 17439 | 141173 | 1604
With the selected technological parameters, virtually all fourth instances (-C) will be excluded from the calculation after the first pass of the branch-and-bound algorithm according to the condition .

## Slide 19
Performance
Subtask | Time, s | Layers | Prefixes | LB0 | LBmax | Solution
p3xl_1-A | 70072 | 29 | 538704 | 1328 | 2130 | 2283
p3xl_1-B | 271 | 28 | 18363 | 1304 | 2140 | 2302
p3xl_2-A | 30756 | 10 | 261442 | 932 | 1629 | Timeout
p3xl_2-B | 22433 | 14 | 253358 | 892 | 1198 | Timeout
p3xl_3-A | 16 | 2 | 86 | 1192 | 1271 | Timeout
p3xl_3-B | 35175 | 28 | 345857 | 1156 | 1835 | 2012
p3xl_4-A | 12541 | 8 | 185483 | 938 | 1110 | Timeout
p3xl_5-A | 10317 | 7 | 194378 | 1919 | 2129 | Timeout
p3xl_5-B | 42097 | 8 | 327747 | 1915 | 2117 | Timeout
Subtask | Time, s | Layers | Prefixes | LB0 | LBmax | Solution
p3xl_1-A | 92 | 15 | 652 | 1328 | 1736 | Stop
p3xl_1-B | 75 | 9 | 61 | 1304 | 1473 | Stop
p3xl_2-A | 199 | 11 | 85 | 932 | 1086 | Stop
p3xl_2-B | 84 | 3 | 17 | 892 | 897 | Stop
p3xl_3-A | 61 | 9 | 108 | 1192 | 1306 | Stop
p3xl_3-B | 49 | 8 | 44 | 1156 | 1253 | Stop
p3xl_4-A | 78 | 8 | 106 | 938 | 1110 | Stop
p3xl_5-A | 1779 | 23 | 76269 | 1919 | 2637 | Stop
p3xl_5-B | 73 | 8 | 45 | 1915 | 2117 | Stop
Independent solution of subtasks
Collaborative solution of subtasks

## Slide 20
Conclusion
A new algorithm for solving the cutting tool routing problem for the class of GSCCP routing problems is proposed
  A cooperative pruning mechanism has been developed to radically reduce computational complexity along with size and depth of search tree
Performance of new algorithm heavily depends on
  technological parameters of the equipment
  cutting allowance
  geometry of the “bridges”
  Deserves further investigation
Computational complexity of GSCCP algorithms may be comparable to well-studied TSP/GTSP algorithms
  Opens possibility to explore full ICP routing problem

## Slide 21
Contacts
Thank you for your attention!
Stanislav Ukolov
Institute of New Materials and Technologies, Ural Federal University, Yekaterinburg, Russia
s.s.ukolov@urfu.ru
Intelligent and Fuzzy Systems (INFUS 2024)
July 16 – 18, 2024
Istanbul , Turkey