## Slide 1
Some Models of Tool Path Optimization Problem for Sheet Metal Cutting Machines
Petrovac, Montenegro
October, 1st-5th
Alexander Petunin, Eugeny Ivanko, Efim Polishuk, Pavel Chentsov, Stanislav Ukolov
IX International Conference
“Optimization and Applications”
OPTIMA 2018
Notes: 1

## Slide 2
1. Statement of the problem of cutter head path optimization for the computer numerical control (CNC) sheet metal cutting equipment. Objective function (time of cutting and cost of cutting).
2. Classification of tool path optimization problems (CCP, ECP, ICP, GTSP). Classification of cutting techniques.
3. Mathematical formalization for tool path problem based on the concept of cutting segment. Extending of the tool path problem classification (SCCP).
4. Generalized SCCP.
5. Development of new algorithms:
5.1. Exact algorithm for GTSP case using special scheme of dynamic programming. Heuristic algorithm for GTSP case with additional constraints.
5.2. Approximate algorithm for SCCP case.
5.3. Approximate algorithm for ECP case (method allowing to reduce the tool path problems that do not include embedded contours and allow partial cutting to the TSP with a special distance matrix).
Abstract

## Slide 3
NC program development
Development of NC programs for CNC sheet cutting machine includes two optimization problems:
Nesting: placement of parts onto plate
2)Tool path problem: tool path routing and choosing tool path according to some optimization criteria

## Slide 4
1
2
3
Initial point
Pierce point
Tool switching off point
Airtime motion
Cutting segments
Contour entry point
Tool path components
Lead-out
Lead-in

## Slide 5
Definition of tool path (route)
Parts:
…
Closed contours:
…
Tool path components:
  - pierce points,
  - segment entry points
  - tool off points
Definition 1: Cutting segment is trajectory between pierce point and tool off point
Note: Segment has a direction at every point.
Definition 2: ,
where - sequence of segments cutting.
Example of route containing 24 cutting segments
n = 24, N = 30, K = 24
Brown parts are cut by one segment
Petunin, Aleksandr A. (2015). Modeling of tool path for the CNC sheet cutting machines// AIP conference proceedings. 41st International Conference on Applications of Mathematics in Engineering and Economics (AMEE), Sozopol, BULGARIA, JUN 08-13, 2015, 1690., pp.060002-1 – 060002-7.

## Slide 6
Cutting techniques
Standard cutting (every closed contour is in its own cutting segment)
Multi-contour cutting (some segments contain several contours)
Multi-segment cutting (one contour is cut by several cutting segments)
1
2
Chain cutting
Snake cutting
1
2
3
4
5
6
8
9
7
1
Bridge cutting
Common edge cutting
Jumper cutting

## Slide 7
Objective functions
Where:
Loff – Length of airtime motion
Lon – Length of cutting segments
Con – Cost of airtime motion unit
Coff – Cost of cutting unit
Cpt – Piercing cost
Voff – Speed of airtime motion
Von – Speed of cutting
Npt – Number of piercing points
tpt – Time of piercing
Cutting cost
Cutting time
1
2
3
Initial point

## Slide 8
Problem classification
CCP: Continuous Cutting Problem
ECP: Endpoint Cutting Problem
ICP: Intermittent Cutting Problem
GTSP: Generalized Traveling Salesman Problem
Dewil, R., Vansteenwegen, P., Cattrysse, D. (2014) Construction heuristics for generating tool paths for laser cutters. International Journal of Production Research, Mar. 2014, 1-20.

## Slide 9
Mathematical formalization
Definition 3: Basic segment is part of cutting segment without lead-in and lead-out
Note: Basic segment has no direction.
When basis segment contains one or more closed contours, direction of cutting (“+” for clockwise, “-” for counter clockwise) must be specified for each of them.
Every basic segments contains list of its closed contours (may be empty). is length of this list.
where (cutting direction).

## Slide 10
Technological constraints
Static ones:
  Precedence constraint
  Piercing points coordinates
  …
Dynamic ones:
  Part Hardness Rule
  Sheet Hardness Rules
  …
Thermal deformations

## Slide 11
Precedence constraint
Yellow
Red
Blue
Gray
  When the external contour contains one or more internal contour(s), that external contour must be cut after the cutting of all internal contours
  If the internal contour of part contains the external contour(s) of another part(s), then the latter parts should be cut first
Permutation:

## Slide 12
Piercing constraint
δ
Δ
Mi: Piercing point
Parti
Lead-in
Lead-out
M*i: Tool off point
Equidistant contour
Partj
Feasible area

## Slide 13
Part Hardness Rule
6
2
3
4
5
1
7
8
9
Detail | Piercing point | CW | CCW
I | 1 | + | ×
 | 2 | × | ×
 | 3 | × | +
 | 4 | + | +
II | 4 | + | ×
 | 5 | × | ×
 | 6 | × | +
 | 7 | + | +
III | 6 | × | ×
 | 7 | + | ×
 | 8 | × | +
 | 9 | × | ×
Cutting path should start next to sheet border or previous cuts
End of cutting should happen near “hard” (not cut yet) sheet zone

## Slide 14
Formalization
The “Hardness” area (the end of detail cutting path) should lay in not cut yet sheet zone.
OK
BAD

## Slide 15
Sheet Hardness Rules
Start from:
  Long narrow parts
  Nested zone
  Small parts
Avoid:
  Uncut ‘islands’
  Narrow uncut zones

## Slide 16
SCCP

## Slide 17
Generalized SCCP
Nesting
SCCP1
SCCP2
SCCPN
SCCP4
SCCP3
…
…
Parts = 56
Segments = 87
=10.592 m
Parts = 56
Segments = 79
=10.226 m
Solution of generalized SCCP
SCCP Ensemble

## Slide 18
Algorithms
  GTSP
    Exact algorithm based on a dynamic programming (up to 30 segments / “megalopolises”)
    Genetic algorithm
    Iterative greedy algorithm (with Part Hardness Rule)
    Iterative greedy algorithm with tool path modification using Bellman’s scheme
    Special option of iterative greedy algorithm for the accounting of a Sheet Hardness Rules
  CCP
    Dual relaxation
  SCCP
    Reduction to GTSP
    Reduction to CCP

## Slide 19
CCP Heuristic
Discrete optimization
Continuous optimization
Precedence constraint
Inner contours (holes) before outers (e.g. 11, 12 & 13)
Inner parts (inside holes) before containers (e.g. 6, 9, 10 before 13)

## Slide 20
Continuous relaxation
Fermat principle
Relaxation
Permutation - fixed
For
Fixed
Processing:
  Sequential
  Random
  Parallel

## Slide 21
Discrete relaxation
Relaxation
Initial permutation
Apply transformation:
  Swap
  Rotate
  Swap blocks with
  Shift block to
  …
Adjust for new permutation
  Apply continuous relaxation
Find
If :
Repeat until converged

## Slide 22
Precedence constraint
C2
C1
C3
C4
C1
C2
C1
C3
C4
C2
C3
C4
M2
M3
M4
M0
C2
C3
C4
M2
M3
M4
M0
M1

## Slide 23
Numerical experiments
Result of dual relaxation
=7.727 m
Exact solution of GTSP
=7.729 m
Straight line
Broken line

## Slide 24
Thank you for your attention!
Alexander A. Petunin
a.a.petunin@urfu.ru
620002, Mira street, 19
Ural Federal University
Yekaterinburg, Russia