## Slide 1
Iterative algorithm for the generalized segmental continuous cutting problem with optimization time constraint
Intelligent and Fuzzy Systems (INFUS 2024)
July 16 – 18, 2024
Istanbul , Turkey
Alexander Petunin, Stanislav Ukolov

## Slide 2
Control program development
for sheet cutting machines
Maximal material utilization
Minimal path cost in terms of money and resources, including cutting time
Nesting
Tool path routing
NC Program generation

## Slide 3
Classification of
tool path routing problems
Continuum of piercing points
GSCCP
GSCCP
TSP
GTSP
CCP
ECP
SCCP
ICP
GSCCP
Finite set of piercing points
Fixed piercing points

## Slide 4
Definition of tool path (route) by cutting segments
Parts:
…
Closed contours:
…
Tool path components:
  - pierce points,
  - segment entry points
  - tool off points
Definition 1: Cutting segment is trajectory between pierce point and tool off point
Note: Segment has a direction at every point.
Definition 2: ,
where - sequence of segments cutting.
Example of route containing 24 cutting segments
n = 24, N = 30, K = 24
Brown parts are cut by one cutting segment

## Slide 5
Definition the Cutting path (Route) by using concept the basic cutting segment
Definition 3: Basic segment is part of cutting segment without lead-in and lead-out
Note: Basic segment has no direction.
When basis segment contains one or more closed contours, direction of cutting (“+” for clockwise, “-” for counter clockwise) must be specified for each of them.
Every basic segments contains list of its closed contours (may be empty). is length of this list.
where (cutting direction).

## Slide 6
Non-standard cutting techniques
Multi-contour cutting - several contours are combined into one
Multi-segment cutting - one of the contours is divided into several parts
Multi-contour cutting of two parts using a “bridge”
In this study, bridges of zero width were used, so when adding one “bridge” to the nesting layout
The number of circuits is reduced by 1
The number of insertion points Npt is reduced by 1 either
The tool stroke length Lon is increased by double bridge length (which is usually chosen as the minimum)
In the practical use of bridges, the stroke length Lon may even decrease, depending on the geometry of the bridge.

## Slide 7
Example of non-trivial cutting segment
Cutting of six pentagons
using single cutting segment
and combined cut technique

## Slide 8
SCCP, GSCCP
Definition 4: SCCP(Segment Continuous Cutting Problem) is a problem with fixed number K and fixed set of Basic segments
Lead-in 1
Lead-out 1
Lead-out 2
Lead-in 2
In Fig. two basic segments are allocated with dashed lines of orange and yellow color.
…are Basic segments and N=K then SCCP is equivalent to CCP
Definition 5: GSCCP (Generalized SCCP) is { SCCPi i=1,2,…,T }
Thus, by introducing the class of GSCCP, we have significantly expanded the existing classification of tool path problem for CNC sheet cutting machines. Actually SCCP and GSCCP are subclasses ICP containing all tasks with finite sets of basic cutting segments, i.e. CCP SCCP GSCCP ICP
Basic segment 1
Basic segment 2

## Slide 9
Example of GSCCP task
Standard Cutting Technique:
45 base segments
Introducing Multi-Contour Cutting:
39 base segments
Reduce to GTSP:
425 possible pierce points

## Slide 10
Two optimization criteria
Cost of cutting process Fcost = where:
Loff — length of tool path with the switched off cutting tool (idle tool path, blue color);
Coff — cost of unit length of tool path with the switched off cutting tool;
Lon — length of tool path with the switched on cutting tool (including length lead-in and lead-out, red color);
Con — cost of unit of a path with the switched on cutting tool;
Npt — number of pierces;
Cpt — cost of one pierce.
Time of cutting process tcut=
where:
Von — speed of cutting process with the switched on cutting tool;
Voff — speed of tool’s movement with the switched off cutting tool;
ton — time for one piercing of sheet material.

## Slide 11
Continuous Cutting Problem
C1
C2
C3
C4
C5
M0
M1
M3
Mn+1
Given:
  Straight line segments
  Circular arcs
  No intersections
  Outside all contours
Find:
Permutation
Objective function:
Piercing points
Air move length

## Slide 12
Precedence Constraint
Other technological constraints exist
Ca
Cb
ia<ib
Ca
Cb
ia>ib

## Slide 13
CCP Heuristic (CCP-Relax Algorithm)
Remove “outer” contours
Continuous optimization
Discrete optimization (pluggable)
Put “outer” contours back

## Slide 14
Removing outer contours
Outer contour
Inner
contour

## Slide 15
Continuous optimization
Mi-1
Mi+1
Ci-1
Ci+1
Ci
Mi
M’i
Mi-1
Mi+1
Ci-1
Ci+1
Ci
Mi
M’i
M*i-1
Choose random
do
  for i = 1 to n: find :
until converged (with some tolerance )
Fixed permutation
Find
Minimize

## Slide 16
Discrete optimization
Variable Neighborhood Search*
Choose random permutation
while :
  if
  else
end
* Hansen, P., Mladenovic, N., and Moreno Perez, J.A. (2010). Variable neighbourhood search: methods and applications. Annals of Operations Research, 175(1), 367 - 407.
Continuous optimization

## Slide 17
Outer contours
Outer contour
Mi
Mi-1
Mi-2
Mi+1
Mi+2
Extra piercing point
Length is preserved
Remains optimal

## Slide 18
Counter example
C1
C2
M0
M3
1 m
1 m
0.2 m
3 m
1 m
1.8 m
Local
optimum
Global
Optimum:

## Slide 19
Local minimum
– polygons
gives minimal :
Let
  On the same segment
Mi
Mi+1
Mi+2
Mi-1
M’i
M’i+1
Mi(s)
Mi+1(t)
Ci
Ci+1

## Slide 20
Local minimum cases
Ci
Mi-1
Mi+1
Mi
Ci
M*i-1
Mi+1
Mi
Mi-1
Ci
Mi-1
Mi+1
Mi
Mi+2
Ci+1
or
  vs
  or
  or

## Slide 21
Global minimum
Mi-1
Mi+1
Mi
Ci
Ci
Mi
Mi-1
Mi+1
Mi
Mi+1
Mi+2
Mi-1
M’i
M’i+1
Mi(s)
Mi+1(t)

## Slide 22
Global minimum cases
Mi-1
Mi+1
Mi
Ci
Ci
Mi
Mi-1
Mi+1
Ci
Mi-1
Mi+1
Mi
Edge case
Corner case
Convex contour

## Slide 23
Numerical experiments
Job | #229 | #464 | #3211
Parts | 11 | 14 | 17
Contours | 12 | 21 | 22
Lon, m | 24.609 | 21.717 | 25.051
Pierce points | 491 | 429 | 493
GTSP’s Loff, m | 7.729 | 4.743 | 4.557
CCP’s Loff, m | 7.727 | 4.706 | 4.536
GTSP (discrete)
CCP (continuous + discrete)

## Slide 24
Large scale example
Job | 20205
# Parts | 115
# Contours | 198
# GTSP points | 3917
GTSP toolpath length | 26.098
CCP toolpath length | 25.987

## Slide 25
Using Relax_CCP Algorithm for solution of SCCP and GSCCP
(a) DP_GTSP
An example of using the DP_GTSP (a) and Relax_CCP (b) algorithms for solution GSCCP
(b) Relax_CCP

## Slide 26
Solving GSCCP:
Greedy vs CCP-Relax
Standard
Cutting Technique:
45 base segments
Multi-Contour Cutting:
39 base segments
Greedy
GTSP Solver
CCP-Relax
Solver

## Slide 27
Conclusion
Continuous Cutting Problem is considered
  With Precedence Constraint
New heuristic for CCP as well as SCCP, GSCCP is proposed
  Both continuous and discrete optimization
  Different discrete optimizators allowed
Continuous optimization solution
  Local minimum – proved
  Global minimum conditions
    Verified easily
Further research
  Extra constraints on piercing point positions
  Using other GTSP solver for discrete part

## Slide 28
Contacts
Thank you for your attention!
Stanislav Ukolov
Institute of New Materials and Technologies, Ural Federal University, Yekaterinburg, Russia
s.s.ukolov@urfu.ru
Intelligent and Fuzzy Systems (INFUS 2024)
July 16 – 18, 2024
Istanbul , Turkey